## Slide 1: CARE-O-BOT
Objective: Demonstrate the behavior of a selected robot in a defined scenario.
Scenario:
Elder person’s home.
Robot programmed to take care of the elder person.
Milestone Requirements:
Present a home environment with:
  A fixed robot.
  A mobile robot.
Mobile robot's capability to move within the environment.
Final Demonstration Requirements:
Mobile robot must:
  Move from one room to the elder person.
  Perform a selected task (transport a glass to the elder’s bed and assist in drinking).

## Slide 2: Webots Environment Creation
Webots is a 3D simulation software for robotics modeling and testing.
Includes a home environment setup for elderly care.
Simulated household objects: Fridge, oven, furniture, and hospital bed.
Two robots: Fixed robotic arm (NED 6DOF) and mobile robot (Robotino).

## Slide 3
Robot Description

## Slide 5: A * Algorithm
Utilizes heuristic-based cost calculation for optimal pathfinding
Supports dynamic updates for real-time navigation adjustments
Developed in Python for seamless integration with Webots
Converts the grid into a suitable format and identifies start & end nodes
Considers diagonal movements for improved efficiency
Returns the computed path as a list of coordinates

## Slide 6: Costmap
Essential for representing obstacles and identifying safe zones
Provides a detailed layout of static and dynamic obstacles
Enables informed navigation decisions by integrating with the A* algorithm
Utilizes Webots and specialized costmap generation libraries
Temporary boundary walls define navigation constraints

## Slide 7
The goal is to keep the obstacles out of the circle
Centroid-Based Obstacle Avoidance Polygon
IR values covered to reference world coordinates.
Treating IR values as a polygon.
Finding the centroid of this polygon.
Creates a polygon using IR sensor data
Computes the centroid to determine the best path.
The centroid calculation adjusts the robot’s path dynamically
c

## Slide 8
Pure Pursuit Path Planning
The robot follows a target point along a predefined path.
It looks ahead to anticipate turns and avoid sharp movements.
Uses a look-ahead distance to find the next waypoint.
Adjusts speed and direction dynamically.

## Slide 9
Grid Drawing for Navigation
Each cell represents a navigable area or obstacle.
The robot maps surroundings in real time.
Uses a grid-based model for optimized pathfinding.
The environment is divided into grid cells.
1
2
3
5
4
6
7
8

## Slide 10
Final Nav and Comms

## Slide 11
Ned Robotic Arm Control
range_dict = { "m1": ( 0.8, -0.8, 45, 135 ), # "joint_name": (limit_1, limit_2, angle_1, angle_2)
"m2": ( 1.3, -1.5, 15, 176.57 ),
"m3": ( 1.5, -1.5, 3.43, 176.57 ),
"base": ( 2.8, -2.8, 175, -175),
"twist1": ( 2, -2, -15, 195),
"twist2": ( 2.5, -2.5, -142, 322),
"gripper": ( 0.01 , -0.01 , 0, 1)}

## Slide 12
Ned Robotic Arm Control : Outlook
Generalized Solution for 6DOF Arms
Gradient Descent Optimization
Neural Network-Based Control
Inverse Kinematics Approaches:
Denavit–Hartenberg parameters

## Slide 13
Care - o - Bots
Project_Goal:
  Two robots to be programmed to take care of a person on a bed by assisting them to drink water.
Project_Milestone:
  A home environment with a fixed and a mobile robot in it. The mobile robot must be able to move within this environment.
Final_Demonstration:
  The robot must be able to move from one room to the elder person, perform a selected task and roll back. The task here is to transport a glass to the elder’s bed and hold them the drink while drinking.

## Slide 14
Robotino:
  Mobile robot powered with 3 Mecanum Wheels
  9 IR Sensors
  1 Bump Sensor
  Accelerometer
  Compass
Ned:
  6DOV Robotic Arm

## Slide 15
VA
VB
VC
VX = VA − VB cos(60˚) + VC cos(30˚)
− VB cos(60˚)
+ VC cos(30˚)
x
y
VY = −VB sin(60˚) + VC cos(30˚)
r . ω = VA + VB + VC
Kinematics of Omni-Directional Wheels
Omni-Directional
Mecanum

## Slide 16
The goal is to keep the obstacles out oV the circle
When: Target point Dist < Radius1 Then: Move point to the away(?)
When: Target point Dist < Radius1 Then: cannot reach, target next point.
c
Obstacle Avoidance Polygon
IR values covered to reference world coordinates.
Treating IR values as a polygon.
Finding the centroid of this polygon.

## Slide 17
Grid Cost Mapping
Lower costs further away from the walls
The path algorithm will prefer the lower costs.
Normalizes at the end.
Euclidean Distance Transform

## Slide 18
Path Finding
A* Search Algorithm
Uses the cost map generated by edt.
Diagonal Search enabled
Pure Pursuit
Look Ahead at bit
Start from the nearest path point

## Slide 19
c
c
The goal is to keep the obstacles out oV the circle
When: Target point Dist < Radius1 Then: Move point to the away(?)
When: Target point Dist < Radius1 Then: cannot reach, target next point.

## Slide 21
1m = 0.90436 gps
1m = (600/10) pxl